## Slide 1
N5 Fluid Mechanics

## Slide 2
www.futuremanagers.com
DEFINITION OF A FLUID
A substance in the liquid or gas phase is referred to as a fluid. A fluid differs from a solid in that a solid can resist an applied shear stress by deforming by a small amount, whereas a fluid deforms continuously (flows) under the influence of shear stress, no matter how small. The amount of flow that takes place is dependent on various properties of the fluid.
  Module 1: Properties of fluids

## Slide 3
www.futuremanagers.com
Module 1: Properties of fluids (continued)
PHYSICAL PROPERTIES OF A FLUID: DENSITY
The density of a fluid is defined as its mass per unit volume and its units are
kg/m3.

## Slide 4
www.futuremanagers.com
Module 1: Properties of fluids (continued)
PHYSICAL PROPERTIES OF A FLUID: SPECIFIC WEIGHT
The specific weight of a fluid is defined as its weight per unit volume and its
units are N/m3.

## Slide 5
www.futuremanagers.com
Module 1: Properties of fluids (continued)
PHYSICAL PROPERTIES OF A FLUID: COMPRESSIBILITY
The compressibility of a fluid is its ability to change its volume under pressure. Compressibility of a liquid is defined as the reciprocal of its bulk modulus (K). Bulk modulus is the ratio between the change in pressure and the volumetric strain and its unit is Pa.

## Slide 6
www.futuremanagers.com
Module 1: Properties of fluids (continued)
PHYSICAL PROPERTIES OF A FLUID: VISCOSITY
The viscosity of a fluid is a measurement of the fluid’s resistance to flow and its units are Pa.s. It is also referred to as dynamic viscosity or absolute viscosity.

## Slide 7
www.futuremanagers.com
Module 1: Properties of fluids (continued)
PHYSICAL PROPERTIES OF A FLUID: SURFACE TENSION
Surface tension is the tension of the surface film of a liquid caused by the attraction of the particles in the surface layer by the bulk of the liquid, which tends to minimise the surface area. This property enables objects with a density higher that water to float on a water surface without becoming even partially submerged.

## Slide 8
www.futuremanagers.com
INTRODUCTION
Pressure systems refer to regions within a fluid where the pressure varies. Pressure is defined as the force per unit area and is a crucial concept in understanding the behaviour of fluids. Fluids can include liquids and gases. The study of pressure systems helps explain how fluids move and interact within different environments.
  Module 2: Pressure systems

## Slide 9
www.futuremanagers.com
Module 2: Pressure systems (continued)
STATIC PRESSURE
Static pressure is the pressure exerted by a fluid at rest and is measured in Pascal. The static pressure in a fluid depends on the height and the specific weight of the fluid. This is the reason why the pressure in a liquid increase with depth and the atmospheric pressure decrease with altitude.

## Slide 10
www.futuremanagers.com
Module 2: Pressure systems (continued)
TYPES OF PRESSURE
The different types of pressure are:
Atmospheric pressure;
Gauge pressure;
Absolute pressure;
Vapour pressure.

## Slide 11
www.futuremanagers.com
Module 2: Pressure systems (continued)
PRESSURE CALCULATIONS ON MANOMETERS AS PRESSURE
MEASURING DEVICES
Manometers are used for measuring pressures by balancing the fluid column of the fluid against another column of fluid with known density. Manometers can be classified and further categorised into two types:
Simple manometers; and
Differential manometers.

## Slide 12
www.futuremanagers.com
INTRODUCTION
A simple hydraulic system refers to a basic mechanism that uses the principles of fluid dynamics to transmit force or energy. Hydraulic systems use a fluid, typically oil or water, to transmit power from one point to another. These systems are widely used in various applications, ranging from heavy machinery and industrial equipment to automotive systems and small tools.
  Module 3: Simple hydraulics systems

## Slide 13
www.futuremanagers.com
Module 3: Simple hydraulics systems (continued)
ACTUATING CYLINDERS
Hydraulic systems like a single hydraulic cylinder, hydraulic jack, hydraulic lift, hydraulic brake system in a vehicle are all examples where Pascal’s principle is applied. Actuating means to start or put something into action.

## Slide 14
www.futuremanagers.com
Module 3: Simple hydraulics systems (continued)
HYDRAULIC JACKS
The hydraulic jack, hydraulic lift and hydraulic brake system in a car are all
examples where the hydraulic system with a mechanical advantage is used.

## Slide 15
www.futuremanagers.com
Module 3: Simple hydraulics systems (continued)
PRESSURE INTENSIFIERS
A pressure intensifier boosts hydraulic pressure generating a small quantity of high-pressure fluid from a large quantity of low-pressure fluid.

## Slide 16
www.futuremanagers.com
Module 3: Simple hydraulics systems (continued)
ROTATING SHAFTS AND PISTONS
When a shaft is rotating in journal bearings, there will be a viscous resistance
acting against the rotation resulting in a loss in torque and power.

## Slide 17
www.futuremanagers.com
INTRODUCTION
This can also be referred to as hydrostatic forces on rectangular and circular tanks containing only one type of fluid.
  Module 4: Hydrostatic forces on submerged areas

## Slide 18
www.futuremanagers.com
Module 4: Hydrostatic forces on submerged areas (continued)
HYDROSTATIC FORCE ON SIMPLE, FULL RECTANGULAR- AND CYLINDRICAL TANKS POSITIONED VERTICALLY CONTAINING THE SAME FLUID MEDIUM AND CENTRE OF PRESSURE
This can also be referred to as hydrostatic forces on rectangular and circular tanks containing two types of fluid. If a tank contains two immiscible fluids, which means that the fluid with the least density will float on top of the denser fluid, the calculations becomes a bit more complicated.

## Slide 19
www.futuremanagers.com
Module 4: Hydrostatic forces on submerged areas (continued)
TOTAL FORCE ON RECTANGULAR AND CYLINDRICAL TANKS
POSITIONED VERTICALLY AND CONTAINING ONLY TWO FLUID
MEDIUMS AND THEIR CENTRES OF PRESSURE
This can also be referred to as hydrostatic forces on plane submerged surfaces.

## Slide 20
www.futuremanagers.com
INTRODUCTION
A solid body dropped into a fluid will sink, float, or remain at rest at any point
in the fluid, depending on its density relative to the density of the fluid. Note
that when the relative density is equal to or greater than one, the floating body becomes completely submerged.
  Module 5: Buoyancy and stability of floating and immersed bodies

## Slide 21
www.futuremanagers.com
Module 5: Buoyancy and stability of floating and immersed bodies (continued)
ARCHIMEDES’ PRINCIPLE
The magnitude of the buoyant force acting on an object that is floating or
submerged in a fluid can be determined by Archimedes’ principle which states:
“When a body is immersed in a fluid either wholly or partially, it is lifted up by
a force which is equal to the weight of the fluid displaced by the body and it acts upwards through the centroid of the displaced volume.”

## Slide 22
www.futuremanagers.com
Module 5: Buoyancy and stability of floating and immersed bodies (continued)
BUOYANCY
The tendency of an immersed body to be lifted up in the fluid due to an upward force opposite to the action of gravity is known as buoyancy. A solid body dropped into a fluid will sink, float, or remain at rest at any point in the fluid.

## Slide 23
www.futuremanagers.com
Module 5: Buoyancy and stability of floating and immersed bodies (continued)
STABILITY
Stability refers to the ability of a body in a fluid to return to its original position
after being tilted about a horizontal axis. The weight of the body acts vertically downwards through the centre of gravity of the body and the force of buoyancy acts vertically upwards through the centre of gravity of the displaced fluid, which is called the centre of buoyancy.

## Slide 24
www.futuremanagers.com
Module 5: Buoyancy and stability of floating and immersed bodies (continued)
TYPES OF STABILITY
Stable: The buoyant force causes a restoring moment which will bring the
floating object back to its original position if displaced.
Neutral: The centre of gravity and the centre of buoyancy coincide.
Unstable: The buoyant force causes an overturning moment which will
cause the floating object to topple over.

## Slide 25
www.futuremanagers.com
INTRODUCTION
Fluid flow is a part of fluid mechanics that deals with the dynamics of fluids. The motion of a fluid subjected to unbalanced forces is known as fluid dynamics. As long as unbalanced pressures are applied, this motion will continue.
  Module 6: Fluid in motion

## Slide 26
www.futuremanagers.com
Module 6: Fluid in motion (continued)
THE NATURE OF FLUIDS AND TYPES FLOW
Flow patterns: A fluid consists of a large number of individual particles moving in the general direction of flow. The velocity of any particle is a vector quantity having magnitude and direction which may vary over time.

## Slide 27
www.futuremanagers.com
Module 6: Fluid in motion (continued)
FLOW TYPES
Steady flow;
Unsteady flow;
Uniform flow;
Non-uniform flow;
Laminar flow;
Turbulent flow.

## Slide 28
www.futuremanagers.com
Module 6: Fluid in motion (continued)
REYNOLDS NUMBER
Reynolds number is a dimensionless quantity that helps predict fluid flow
patterns in different situations by measuring the ratio between different forces.

## Slide 29
www.futuremanagers.com
Module 6: Fluid in motion (continued)
FLUID IN MOTION CALCULATIONS
Hydrodynamics deals with the flow of water in pipes or open channels. The main difference between pipe flow and open-channel flow is that pipe flow is regarded as fluid that flows in closed conduits and are entirely in contact with rigid boundaries. Open-channel flows, on the other hand, are those whose boundaries are not entirely a solid and rigid material. Due to the differences in those boundaries, different forces affect the two types of flows and different formulae are therefore used in calculations.

## Slide 30
www.futuremanagers.com
Module 6: Fluid in motion (continued)
CONSERVATION OF ENERGY IN FLUIDS
The law of conservation of energy states that energy can be neither created nor destroyed, only converted from one kind of energy into another. In other words, the total energy of an isolated system remains constant. The same principle applies to fluid mechanics.

## Slide 31
www.futuremanagers.com
INTRODUCTION
Measuring the flow of liquids is a critical need in many industrial applications. In some operations, the ability to conduct accurate flow measurements is so important that it can make the difference between making a profit or taking a loss. Flow measurement involves using flow meters that measure the amount of fluid moving through a pipe, channel or space by measuring volumetric flow rates.
  Module 7: Flow measurement using instruments

## Slide 32
www.futuremanagers.com
Module 7: Flow measurement using instruments (continued)
FLOW MEASUREMENT
Flow measurement involves using flow meters that measure the amount of fluid moving through a pipe, channel or space by measuring volumetric flow rates. There are many different types of flow meters that can be utilised depending on the nature of the application.

## Slide 33
www.futuremanagers.com
Module 7: Flow measurement using instruments (continued)
FLOW MEASUREMENT: MECHANICAL FLOWMETER
Mechanical flow meters consist of a moving part or rotational device. The liquid that passes through the mechanical flowmeter induces rotation or displacement of the moving part. The flow rate that is created in the flowmeter is proportional to the movement of the device. The rotameter is an example of this type of flow meter.

## Slide 34
www.futuremanagers.com
Module 7: Flow measurement using instruments (continued)
FLOW MEASUREMENT: PRESSURE DROP FLOWMETER
With most pressure drop-based flow measurement instruments, the flow rate is determined by measuring the fluid’s velocity or the change in kinetic energy. Velocity depends on the pressure differential that is forcing the fluid through the pipe. Because the pipe’s cross-sectional area is known and remains constant, the average velocity is an indication of the flow rate. The pitot tube and the venturi meter are examples of this type of flow meter.

## Slide 35
www.futuremanagers.com
Module 7: Flow measurement using instruments (continued)
PITOT TUBE
Pitot tubes are widely used to determine a boat’s water speed, the airspeed of an aircraft, and measure air, liquid and gas flow velocities in various industrial applications. A simple pitot tube consists of a glass tube bent at right angle. The bent part is placed in the centre of the pipe towards the flow of the fluid.

## Slide 36
www.futuremanagers.com
Module 7: Flow measurement using instruments (continued)
VENTURI METER
A Venturi meter is a type of differential pressure flow meter that generates flow measurement by measuring the pressure difference at two different locations in a pipe. This pressure difference is created by decreasing the diameter of the pipe, which causes an increase in flow velocity and a corresponding drop in pressure.

## Slide 37
www.futuremanagers.com
INTRODUCTION
In big distribution networks, there are very long lengths of pipes and numerous apparatus in the pipe systems. The losses caused by long lengths of pipes and the existence of fittings, bends and valves in pipelines cannot be ignored when the pressure loss and power needed to drive the fluid need to be calculated.
  Module 8: Pipeline systems

## Slide 38
www.futuremanagers.com
Module 8: Pipeline systems (continued)
LOSSES IN PIPELINES
The kinds of losses that exist in pipelines can be categorised into minor losses (caused by shock) and major losses (due to friction).

## Slide 39
www.futuremanagers.com
Module 8: Pipeline systems (continued)
LOSSES IN PIPELINES: MINOR LOSSES
Minor losses are caused by the disruption of flow due to the installation of valves, fittings and bends. These losses do not play a major role in losses that occur in a pipeline, but when each loss is added it can still have a significant influence on the total loss in a pipeline.

## Slide 40
www.futuremanagers.com
Module 8: Pipeline systems (continued)
LOSSES IN PIPELINES: MAJOR LOSSES
Major losses are associated with frictional energy loss that is caused by the viscous effects of the fluid and roughness of the pipe wall. Major losses create a pressure drop along the pipe since the pressure must work to overcome the frictional resistance.

## Slide 41
www.futuremanagers.com
Module 8: Pipeline systems (continued)
EQUIVALENT LENGTH
Another way to describe the hydraulic resistance of valves and fittings is to use an equivalent-length ratio. This requires converting the shock loss within a fitting, bend or valve to an equivalent length of pipe that would produce the same loss due to its loss coefficient.

## Slide 42
www.futuremanagers.com
INTRODUCTION
An orifice is an opening, of any size or shape, in a pipe or at the bottom or side wall of a container through which fluid is discharged. This opening is typically created by placing a plate or a thin edge within a fluid-carrying pipe or container. The shape and size of the orifice plays a crucial role in determining the characteristics of fluid flow through it.
  Module 9: Flow through orifices

## Slide 43
www.futuremanagers.com
Module 9: Flow through orifices (continued)
SMALL ORIFICES
Orifices may be classified based on their size, shape, sharpness and discharge An orifice is known as a small orifice if the head of liquid from the centre of the orifice is more than five times the depth of the orifice.

## Slide 44
www.futuremanagers.com
Module 9: Flow through orifices (continued)
VENA CONTRACTA
Vena contracta is the point in the fluid stream where the cross-sectional area of the stream is the least and fluid velocity is at its maximum. The distance of vena contracta from the orifice is approximately equal to one-half the depth or diameter of the orifice. The stream lines of flow are converging up to the vena contracta and beyond this section the stream lines are parallel.

## Slide 45
www.futuremanagers.com
Module 9: Flow through orifices (continued)
CALCULATIONS FOR ORIFICE FLOW
If the geometric properties of the orifice and the properties of the fluid are known, the orifice can be used to measure flow rates and to calculate all the flow coefficients.

## Slide 46
www.futuremanagers.com
INTRODUCTION
Fluid momentum is a concept in fluid mechanics that describes the motion of
a fluid and its resistance to changes in motion. The design of many hydraulic
structures, such as tapered pipes and bends, as well as blades in pumps and
turbines, depends upon the forces that a fluid flow exerts on them.
  Module 10: Conservation of a momentum (fluid momentum)

## Slide 47
www.futuremanagers.com
Module 10: Conservation of a momentum (fluid momentum) (continued)
FORCE EXERTED BY A JET OF FLUID
When a fluid is supplied by a nozzle, a high velocity jet of fluid is produced which is then used to supply water for firefighting equipment or to drive the vanes of pelton wheels or turbines. The momentum equation is used to determine the resultant force exerted by a jet of fluid on vanes as the flow changes its direction or the magnitude of velocity or both.

## Slide 48
www.futuremanagers.com
Module 10: Conservation of a momentum (fluid momentum) (continued)
FORCE ON A STATIONARY PLATE OR VANE
When dealing with stationary vanes, only the jet of fluid is moving and the velocity of the vane is zero. The result is that the total mass flow rate of the jet is effective in the dynamic force exerted on the vane. The velocity after it strikes the stationary vane is dissipated and becomes zero.

## Slide 49
www.futuremanagers.com
Module 10: Conservation of a momentum (fluid momentum) (continued)
FORCE ON A MOVING PLATE OR VANE
When dealing with a single moving vane, the velocity of the jet relative to the vane will determine the effective mass flow rate impacting on the vane. The length of the jet is continually increasing. Part of the fluid leaving the nozzle is required to extend the length of the jet thus reducing the amount of mass flow that strikes the vane.

## Slide 50
www.futuremanagers.com
Module 10: Conservation of a momentum (fluid momentum) (continued)
FORCE EXERTED ON REDUCERS AND BENDS
When dealing with flow in pipelines, two forces need to be considered. The
force due to pressure and the dynamic force due to change in momentum have an influence on the total force exerted on reducers and bends in a pipeline.

## Slide 51
www.futuremanagers.com
INTRODUCTION
Pumps are used to increase the energy level of water in order for it to be raised to a higher level. A reciprocating pump is also known as a positive displacement pump because it discharges a definite quantity of liquid. The delivery of a reciprocating pump is determined by the physical dimensions of the piston diameter and stroke length as well as the speed of the pump.
  Module 11: Reciprocating pumps

## Slide 52
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
CYLINDER
The cylinder serves as a chamber for the liquid to be drawn in at low pressure and delivered at high pressure. It accommodates the reciprocating piston.

## Slide 53
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
PISTON AND PISTON ROD
The piston has seals in order to create a vacuum during the suction stroke and high pressure during the delivery stroke. The piston rod allows the piston to be connected to the connecting rod which is connected to a rotating crank.

## Slide 54
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
CRANK AND CONNECTING ROD
The function of the crank and connecting rod is to convert angular motion of
the electrical motor and crank to linear reciprocating motion for the piston.

## Slide 55
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
SUCTION PIPE
The suction pipe connects the cylinder to the lower liquid level in order for the liquid to be drawn into the cylinder.

## Slide 56
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
DELIVERY PIPE
The delivery pipe connects the cylinder to the upper level in order for the high-pressure liquid to be delivered to the discharge outlet.

## Slide 57
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
SUCTION VALVE
The suction valve allows the low-pressure liquid to flow in one direction only
into the cylinder. It is also known as a non-return valve. The valve is closed
during the delivery stroke.

## Slide 58
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
DELIVERY VALVE
The delivery valve allows the high-pressure liquid to flow in one direction only into the delivery pipe. It is also known as a non-return valve. The valve is closed during the suction stroke.

## Slide 59
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
FOOT VALVE
The foot valve is a non-return valve installed at the suction pipe inlet. The foot valve keeps the fluid trapped in the pipe by preventing the liquid in the suction pipe to drain out due to gravity when the pump is stopped. The pump stays primed, preventing cavitation or even pump burnout when the pump is restarted.

## Slide 60
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
STRAINER
The strainer is an essential part of the pump and is located at the suction pipe inlet. The strainer helps in preventing the entry of solids from the liquid source into the cylinders.

## Slide 61
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
TYPES OF RECIPROCATING PUMPS AND HEADS
Reciprocating pumps can be classified as follows:
According to which side of piston is active; and
According to number of cylinders.

## Slide 62
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
TYPES OF PRESSURE HEADS
In order to determine the pressure and power required by a pump to move a fluid there are certain pressure heads that need to be considered. Some heads are actual vertical distances that can be observed by looking at the water levels of the pump system.

## Slide 63
www.futuremanagers.com
Module 11: Reciprocating pumps (continued)
BASIC CALCULATIONS OF RECIPROCATING PUMPS
The theoretical flow rate of a reciprocating pump depends on the diameter and stroke length of the piston as well as the rotational speed of the crank. The actual flow rate of a reciprocating pump depends on how worn the seals are on the piston.