## Slide 1
Strength of Materials and Structures
N6

## Slide 2
www.futuremanagers.com
SINGLE CYLINDERS
When a cylinder shell is subjected to an internal pressure or external pressure three stresses will develop in the cylinder wall. The three principal stresses at work are radial stress, hoop stress, and longitudinal stress.
Module 1: Thick cylinders

## Slide 3
www.futuremanagers.com
Module 1: Thick cylinders (continued)
COMPOUND CYLINDERS
A compound cylinder consists of two cylinders which are shrunk together to form an inner and outer cylinder. The two cylinders will be shrinking together and can be used like a hub which is shrunk onto a shaft, setting up stresses throughout the cylinder wall thickness.

## Slide 4
www.futuremanagers.com
INTRODUCTION TO SIMPLE CATENARY CABLES
A catenary is the U-shaped curve formed by a heavy inextensible cable, chain or rope of uniform density suspended from its endpoints.
Module 2: Tension in cables

## Slide 5
www.futuremanagers.com
Module 2: Tension in cables (continued)
PARABOLIC CATENARIES
A parabolic catenary is formed when a cable carries a horizontal uniformly distributed load. One such example is a suspension bridge.

## Slide 6
www.futuremanagers.com
INTRODUCTION
There are many examples where shafts are subjected to bending moments and torque simultaneously. One example is a shaft with a pulley, driven by V-belts or a flat belt. The cause of the bending can be due to:
The weight of the pulley;
Tension in the belt; and
The weight of the shaft.
Module 3: Combined bending and twisting of shafts

## Slide 7
www.futuremanagers.com
Module 3: Combined bending and twisting of shafts (continued)
BENDING MOMENTS IN SHAFTS
Shafts are treated as standard beams with loads located at different places on the shaft. Forces which cause bending moments:
The weight of the shaft;
The weight of the pulley; and
The belt tension.

## Slide 8
www.futuremanagers.com
BENDING OF BEAMS
When selecting beams, there are two limits to consider:
The bending moment in the beam must be such that the bending stress does not exceed the material’s proportional limit. The bending stress must be within the limit of proportionality.
The deflection of the beam must be within the safe limit of of the beam’s length.
Module 4: Bending and deflection of beams

## Slide 9
www.futuremanagers.com
Module 4: Bending and deflection of beams (continued)
DEFLECTION AND SLOPE
The effect of load on deflection: If the load increases the deflection will increase, therefore the deflection is directly proportional to the load.

## Slide 10
www.futuremanagers.com
DIRECT AND BENDING STRESSES
When axial forces are applied it causes direct stress as the load is applied directly on the cross section of the member.
Bending stress will occur when the load is applied in such a position that it causes bending to the member, like lateral forces applied to a beam.
Module 5: Combined direct and bending stress

## Slide 11
www.futuremanagers.com
GENERAL SHEAR STRESS
The shearing force at a particular section of a beam is the resultant force of all forces acting on either side of that section.
Module 6: Shear stress in beams

## Slide 12
www.futuremanagers.com
SINGLE SPRING INDEX
The spring index is the ratio between the effective diameter, mean diameter, and the wire diameter.
Module 7: Closed-coiled helical springs

## Slide 13
www.futuremanagers.com
PLANE STRESSES
Tensile stress: Arrows going outwards (taken as positive).
Compressive stresses: Arrows inwards (taken as negative).
Shear stress, which are two pairs of stresses:
  One pair is clockwise and negative.
  One pair is counter-clockwise and positive.
Module 8: Transformation of stress

## Slide 14
www.futuremanagers.com
Module 8: Transformation of stress (continued)
MOHR’S CIRCLE FOR PLANE STRESSES
Stresses are used to draw a stress circle which can determine stresses.
The circle is based on the stress transformation equations and provide a graphical solution to the problem of determining.
Using Mohr’s circle involves:
  Principal stresses;
  Principal planes; and
  Maximum shear stresses.

## Slide 15
www.futuremanagers.com
SHEERLEGS AND TRIPODS
A sheerleg (or shear leg) is a type of crane which consists of two legs of equal length and a backstay, which is longer than the legs.
Tripods differ from sheerlegs as they have three legs and no backstay. A tripod is static with regards to the displacement of the load as it can only lift or lower a load in the same position.
Module 9: Forces in structural frameworks

## Slide 16
www.futuremanagers.com
Module 9: Forces in structural frameworks (continued)
DERRICK CRANES
Derrick cranes usually consist of a distinctive vertical mast that can rotate, and a jib connected at the foot of the mast. By using cables, the crane raises and lowers loads, and this is limited only by the height of the jib. The mast is usually stabilised using guys (cables) that limit the crane’s range of rotation.