## Slide 1
Building and Structural Surveying
N5

## Slide 2
www.futuremanagers.com
INTRODUCTION
Surveying ensures that everything is in the right place on the right alignment and where it is intended be. Without surveying, there would be no tall buildings, bridges or roads. It is a service that ensures columns of buildings are plumb, property lines are defined, structures are aligned, estimates are correct, etc. Understanding the basic principles of surveying is therefore essential in order to understand the discipline.
Module 1: Basic principles of surveying

## Slide 3
www.futuremanagers.com
Module 1: Basic principles of surveying (continued)
DEFINITION OF SURVEYING
Surveying may be defined as the art of determining the relative positions of
points on, above or beneath the surface of the earth with respect to each other by measurement of horizontal distances, vertical distances, angles and directions.

## Slide 4
www.futuremanagers.com
Module 1: Basic principles of surveying (continued)
STAGES IN THE SURVEYING PROCESS
Step 1: Reconnaissance (taking a general view)
During reconnaissance, the surveyor does an overall inspection of the area to be surveyed to obtain a general picture before commencement of any type of field work and measurement. The surveyor will then select the location for control points and decide on the accuracy required for the control and which survey instruments to use for the project.

## Slide 5
www.futuremanagers.com
Module 1: Basic principles of surveying (continued)
STAGES IN THE SURVEYING PROCESS (CONT.)
Step 2: Field work and measurement (observation and measurement)
During this stage, the surveyor will perform all the observations required to accurately determine the control points, and will place and observe any temporary points and record all data in the field book. The surveyor will also do any calculations from the observations, such as angular and linear misclosure, and area and volume calculations.

## Slide 6
www.futuremanagers.com
Module 1: Basic principles of surveying (continued)
STAGES IN THE SURVEYING PROCESS (CONT.)
Step 3: Office work (presentation of data)
At this stage, the data collected and recordings in the field book are decoded
and used to prepare the report, bills of quantities, datasheets, drawings and, in land surveying, plans and maps showing the features on the land, which are then presented to the clients and relevant stakeholders.

## Slide 7
www.futuremanagers.com
Module 1: Basic principles of surveying (continued)
FUNDAMENTAL PRINCIPLES OF SURVEYING
Surveying, in general, is based on a number of principles:
• Working from the whole to a part
• Location of a point by measurement from two points of reference
• Consistency of work
• Independent checks
• Accuracy required.

## Slide 8
www.futuremanagers.com
Module 1: Basic principles of surveying (continued)
ACCURACY AND PRECISION
Because no measurement is ever completely accurate, surveyors strive for both accuracy and precision. These words have different meanings to a surveyor. Accuracy refers to how closely a measurement or observation is to measuring a true value, as measurements and observations are always subject to error. Precision refers to how closely repeated measurements or observations come to duplicating measured or observed values.

## Slide 9
www.futuremanagers.com
Module 1: Basic principles of surveying (continued)
ERRORS IN MEASUREMENT
Mistakes are avoidable blunders that occur because of carelessness or a
temporary mental lapse. They include incorrect readings and booking of
observations as well as the use of erroneous data in calculations. There is no law governing the occurrence of mistakes and no observer is beyond making mistakes.

## Slide 10
www.futuremanagers.com
Module 1: Basic principles of surveying (continued)
ERRORS IN MEASUREMENT (CONT.)
Constant errors are errors that, in all measures under the same circumstances, have the same magnitude and algebraic sign. The errors can be caused by either the apparatus itself or external circumstances to the apparatus. Examples of constant errors are:
  • measuring with a tape that is too long or too short; and
  • using a theodolite or dumpy level with a collimating error.

## Slide 11
www.futuremanagers.com
Module 1: Basic principles of surveying (continued)
ERRORS IN MEASUREMENT (CONT.)
Systematic errors are caused by the surveying equipment, observation methods, and certain environmental factors such as variations in temperature, humidity, pressure, current velocity, curvature, and refraction. Under the same measurement conditions, these errors will have the same magnitude and direction (positive or negative). Because systematic errors are repetitive and tend to accumulate in a series of measurements, they are also referred to as cumulative errors.

## Slide 12
www.futuremanagers.com
INTRODUCTION
Distance measurement is considered to be the most fundamental of all surveying operations. It is a process of measuring distances between points on a surface using a chain or tape. It is done based on the linear surveying principle that states: if the distance between two points is measured, the points are fixed. This module details the methods of overcoming field challenges and plotting of chain surveys.
Module 2: Linear measurements

## Slide 13
www.futuremanagers.com
ERRORS IN MEASUREMENT AND CORRECTIONS
To compensate for the unavoidable errors in measurement, it is generally
necessary to apply corrections to measurements made by direct linear methods.
Module 2: Linear measurements (continued)

## Slide 14
www.futuremanagers.com
LINEAR MEASUREMENT OBSTACLES
Linear measurement lines should, as far as possible, be arranged to avoid
obstacles. However, occasionally obstacles are unavoidable, even after a careful preliminary survey. The following are some of these obstacles:
• Measuring a horizontal distance on a slope
• Measuring slope angle using a clinometer
• Measuring around a pond or across a river or a busy road
• Measuring when a building obstructs vision.
Module 2: Linear measurements (continued)

## Slide 15
www.futuremanagers.com
CHAINING OR TAPING
Surveying lines are measured using a chain or tape as the principal instrument for the accurate determination of lengths.
Module 2: Linear measurements (continued)

## Slide 16
www.futuremanagers.com
PLOTTING SURVEYS
Plotting means to represent on paper, to a suitable scale, the previously surveyed objects in accordance with their shape and size.
Plotting commences after the field work has been completed.
Module 2: Linear measurements (continued)

## Slide 17
www.futuremanagers.com
COORDINATES
Coordinates are figures that indicate the distance of the location of a concern
from the two coordinate axes. They are used to describe the exact position of a location on the ground, or on a map or plan.
Module 2: Linear measurements (continued)

## Slide 18
www.futuremanagers.com
INTRODUCTION
Height, or orthometric height, refers to elevation which is defined as the vertical distance along the plumb line, from a point of interest to a reference surface known as the geoid (an imaginary mean sea level surface).
The process of measuring height is called levelling. This module will detail the method involved in measuring, recording and reducing the measurement to establish the position of points on the earth’s surface.
Module 3: Height measurement

## Slide 19
www.futuremanagers.com
LEVELLING TERMINOLOGY
The various important terms to remember in levelling are:
Planes (horizontal, vertical and incline)
Direction of gravity
Level surface
Collimation line
Change point (CP)
Module 3: Height measurement (continued)

## Slide 20
www.futuremanagers.com
Levelling means determining the relative elevations or heights of points using a
dumpy level or automatic level.
DEFINITION AND PURPOSE OF LEVELLING
Module 3: Height measurement (continued)
Levelling means determining the relative elevations or heights of points using a
dumpy level or automatic level.
Levelling is done for all important engineering works and construction projects.

## Slide 21
www.futuremanagers.com
DIFFERENTIAL LEVELLING Differential levelling is a technique used to determine differences in elevation between points that are distant from each other. It requires the use of a surveyor’s level together with a levelling staff.
Module 3: Height measurement (continued)

## Slide 22
www.futuremanagers.com
Module 3: Height measurement (continued)
TRIGONOMETRIC LEVELLING
Trigonometric levelling is a process of levelling in which the elevation of
points or the difference in height between points is measured from the observed horizontal distances and vertical angles in the field.
The trigonometric relations are then used to find the elevation of a point from the angle and horizontal distance.

## Slide 23
www.futuremanagers.com
Module 3: Height measurement (continued)
BAROMETRIC LEVELLING
Barometric levelling is a type of indirect levelling method in which the
differences in the elevation of points are determined from differences in
atmospheric pressure observed with altimeters or barometers at each point.

## Slide 24
www.futuremanagers.com
Module 3: Height measurement (continued)
LEVELLING INSTRUMENTS
Levelling staff – a straight rod, rectangular in cross-section and graduated in metres and millimetres.
Wye level – a surveyor’s levelling instrument that consists of a telescope mounted on two Y-shaped supports and a spirit level mounted under and parallel to the telescope.

## Slide 25
www.futuremanagers.com
Module 3: Height measurement (continued)
LEVELLING INSTRUMENTS (CONT.)
Cooke’s reversible level – a combination of a dumpy level and a Y-level
Cushing’s level – a levelling instrument in which the telescope is rigidly fixed in the collar, as in a dumpy level
Staff bubble – a small, circular bubble on an angle plate that is held against one corner of the staff

## Slide 26
www.futuremanagers.com
Module 3: Height measurement (continued)
LEVELLING INSTRUMENTS (CONT.)
Change plate – a triangular steel plate with a pin at the centre and three corners turned down; it is used to mark the change point position of the staff and to prevent the staff from sinking
Traveller (or boning rod) – used to control an excavation to ensure that it has a uniform depth and is sometimes used with a sighting rail when excavating trenches for drainage pipes

## Slide 27
www.futuremanagers.com
Module 3: Height measurement (continued)
LEVELLING INSTRUMENTS (CONT.)
Dumpy level – provides an accurate line of sight that enables it to be used over long distances for setting up benchmarks for levelling
Tripod – a stand that consists of three legs that are solid-framed; it is used to hold the instrument while surveying
Theodolite – ideal for tacheometric and traverse surveying, but not for
differential surveys

## Slide 28
www.futuremanagers.com
Module 3: Height measurement (continued)
LEVELLING INSTRUMENTS (CONT.)
Tilting level – a level used for precise levelling work
Automatic level – useful in series levelling because it has a compensator which keeps the telescope level

## Slide 29
www.futuremanagers.com
Module 3: Height measurement (continued)
CLASSIFICATION OF A LEVEL TRAVERSE
A level traverse is a series of levels carried out in order to determine the
difference in levels between points on the surface of the ground. It is also called a level run. Level traverses can be classified as closed or open traverses.
A closed level traverse is a series of level runs from a known datum or reduced level. There are two types of closed traverses, namely closed link and closed loop traverses.

## Slide 30
www.futuremanagers.com
Module 3: Height measurement (continued)
ERRORS IN LEVELLING
Errors in levelling are classified as instrumental, personal or natural. They can be reduced by careful adjustment, establishment of field procedures and adhering to these procedures, but they cannot be eliminated.

## Slide 31
www.futuremanagers.com
Module 3: Height measurement (continued)
FLY LEVELLING
Fly levelling is used for transferring levels and the only readings required are the backsight and foresight recordings. The intermediate sight readings are not used, but the distance between readings should not exceed 50 m.
Fly levelling can be helpful when the benchmark is very far from the workstation.

## Slide 32
www.futuremanagers.com
Module 3: Height measurement (continued)
SERIES LEVELLING
Series levelling is used to determine the difference in level between points on the surface of the ground, and the readings required are backsight, foresight and intermediate sight readings.

## Slide 33
www.futuremanagers.com
Module 3: Height measurement (continued)
RISE AND FALL METHOD
In this method, the difference in level between two consecutive points for each instrument set up is obtained by comparing their staff readings. The difference between their staff readings indicates a rise if the backsight staff reading is more than the foresight and a fall if it is less than the foresight. The algebraic sum of rises and falls gives the difference in level between the starting and closing points.

## Slide 34
www.futuremanagers.com
Module 3: Height measurement (continued)
COLLIMATION HEIGHT METHOD
In this method, the instrument height is calculated for the first instrument set
up by adding the backsight to the reduced level of the given benchmark.
The reduced level of the first station is obtained by subtracting its foresight from the instrument height.

## Slide 35
www.futuremanagers.com
Module 3: Height measurement (continued)
CROSS-SECTION LEVELLING
Cross sections are vertical sections of the Earth’s surface taken at right angles to the main survey line or longitudinal section. They are used in construction work such as that of roads, water channels, and railways. The principal purpose is to provide data so that the depth of fill or cut required to bring the existing surface up or down to the elevation required for the project, can be determined.

## Slide 36
www.futuremanagers.com
Module 4: Angular measurement
INTRODUCTION
Measurement of angles is an integral part of surveying. Initially, surveyors used the compasses to define direction, by putting the survey on a magnetic meridian.
Theodolites were developed to allow more accurate measurement of angles,
both vertical and horizontal. This module will detail the instrument and method involved in taking and reducing these measurements.

## Slide 37
www.futuremanagers.com
Module 4: Angular measurement (continued)
PURPOSE OF ANGULAR MEASUREMENT
Horizontal and vertical angles are fundamental measurements in surveying.
The vertical angle is used to obtain the elevation of points and in the reduction of sloping distance to the horizontal. The horizontal angle is used primarily to obtain bearing and direction to a survey control point, topographic detail points, points to be set out or points to be surveyed.

## Slide 38
www.futuremanagers.com
Module 4: Angular measurement (continued)
PURPOSE OF ANGULAR MEASUREMENT (CONT.)
Vertical angular measurements are measured to determine the slope lines from the horizontal plane or level line. Vertical angles are angles measured on a plane perpendicular to the horizontal plane or the plane parallel to the plumb line.

## Slide 39
www.futuremanagers.com
Module 4: Angular measurement (continued)
CLASSIFICATION OF THEODOLITES
Theodolites are classified based on the following the movement of the
on the horizontal axis in a vertical plane and the arrangement for measuring the angles.

## Slide 40
www.futuremanagers.com
Module 4: Angular measurement (continued)
CLASSIFICATION OF THEODOLITES (CONT.)
Transit- and non-transit theodolites are thus classified based on the movement of the telescope on the horizontal axis in a vertical plane.
Vernier- and micrometer theodolites that are so classified based on certain arrangements in the way angles are measured. One uses a vernier and the latter uses a micrometer for these measurements.

## Slide 41
www.futuremanagers.com
Module 4: Angular measurement (continued)
THEODOLITE TERMINOLOGY
Centering – the process of setting up a theodolite on a ground station
Vertical axis – the axis about which the instrument rotates in a horizontal plane
Horizontal axis – the axis of rotation of the telescope in the vertical plane, also known as the trunnion axis
Circle left (CL) – also known as face left; refers to the situation when the vertical circle of the instrument is on the left of the observer when the reading is taken

## Slide 42
www.futuremanagers.com
Module 4: Angular measurement (continued)
THEODOLITE TERMINOLOGY (CONT.)
Circle right (CR) – also known as face right; refers to the situation when the
vertical circle of the instrument is on the right of the observer when the reading is taken
Changing face – the operation of bringing the vertical circle from one side of the observer to the other side of the observer
Swinging the telescope – the process of rotating the telescope about the vertical axis in the horizontal plane

## Slide 43
www.futuremanagers.com
Module 4: Angular measurement (continued)
THEODOLITE TERMINOLOGY (CONT.)
Transiting the telescope – the process of turning the telescope through 180° in the vertical plane about its horizontal axis object glass and the optical centre of the eyepiece
Axis of the bubble tube – an imaginary line tangential to the longitudinal curve of the bubble tube, at its midpoint
Bisecting a point or station – when the vertical hair of the telescope lies in
the middle of the ranging rod placed at the survey station being observed

## Slide 44
www.futuremanagers.com
Module 4: Angular measurement (continued)
COMPUTATION OF HORIZONTAL ANGLES
Suppose that the direction from point A to a point B has to be measured.
• Set up the theodolite at station A, remembering to check for parallax before
any measurement is performed. Once the parallax is removed, bisect point E
with a certain circle reading, sight as close to the bottom of the ranging rod
at B as possible to eliminate any errors caused by non-verticality of the rod
and note the reading as circle left.

## Slide 45
www.futuremanagers.com
Module 4: Angular measurement (continued)
COMPUTATION OF HORIZONTAL ANGLES (CONT.)
• Change the face of the telescope to get the circle right reading and note
the reading.
• The mean direction is then calculated using the following formula:
When the circle right is smaller than 180°, then 180° is added to circle right,
and when the circle right is greater than 180°, then 180° is subtracted from
circle right.

## Slide 46
www.futuremanagers.com
Module 4: Angular measurement (continued)
COMPUTATION OF VERTICAL ANGLES A vertical angle is an angle between the horizontal line and the inclined line
of sight. When it is below the horizontal line, it is called the angle of elevation. When it is below the line of sight, it is called the angle of depression. During computation, if the vertical angle is positive, it is called the angle of elevation. If it is negative, it is called the angle of depression. To eliminate errors, a vertical angle should be observed with circle left and circle right, and the mean of the value computed.

## Slide 47
www.futuremanagers.com
Module 4: Angular measurement (continued)
TACHEOMETRY
Tacheometry is a branch of surveying in which the horizontal and vertical
distances are determined by angular observation using a tacheometer.

## Slide 48
www.futuremanagers.com
Module 4: Angular measurement (continued)
USES OF TACHEOMETRIC SURVEYING
Tacheometric surveying is used for the following:
• Preparing topographic maps or plans where both horizontal and vertical
distances are required;
• Determining differences in elevation between points;
• Measuring the lengths of traverse lines; and
• Locating details for hydrographic survey.

## Slide 49
www.futuremanagers.com
Module 5: Building surveys (continued)
BUILDING REGULATIONS AND BUILDING CONSTRUCTION PRACTICE
Building regulations exist to ensure that buildings are designed and constructed in accordance with the building regulations and related legislation. These regulations set national standards for building work. They cover all aspects of construction, including foundations, damp-proofing, building stability, insulation, ventilation, heating, fire protection and facilities for disabled people in certain types of buildings. Construction companies carrying out building work must comply with the building regulations.

## Slide 50
www.futuremanagers.com
Module 5: Building surveys (continued)
BUILDING CODES
Building codes are regulations governing the design, construction, alteration and maintenance of structures. They specify the minimum requirements to safeguard the health, safety and welfare of buildings’ occupants. They are enforced to make buildings safer to withstand earthquakes and other natural disasters.

## Slide 51
www.futuremanagers.com
Module 5: Building surveys (continued)
BUILDING SURVEYS
A building survey is the in-depth inspection and investigation of a building and the services of a property by a professional surveyor to ensure that they comply with the building regulations and in order for the surveyor to be able to advise a building owner or buyer on the condition of the building.

## Slide 52
www.futuremanagers.com
Module 5: Building surveys (continued)
DESIGN DRAWINGS
Design drawings are done as the first step in the design phase. They are typically visual drawings or representations of the client’s ideas and the designer’s intent.
They allow the architect or designer to communicate their concepts and vision to the contractor.

## Slide 53
www.futuremanagers.com
Module 5: Building surveys (continued)
BUILDING SURVEYS
A building survey is the in-depth inspection and investigation of a building and the services of a property by a professional surveyor to ensure that they comply with the building regulations and in order for the surveyor to be able to advise a building owner or buyer on the condition of the building.

## Slide 54
www.futuremanagers.com
Module 5: Building surveys (continued)
CUTTING AND FILLING
Cutting and filling is the process of moving earth from one place to another
to make the ground level. The term cut is used when earth above the required ground level is removed, and fill is used when earth is used to seal a hollow section to the required level. Most often, the site meant for construction is not level and needs to be modified before any construction can begin, thereby making cutting and filling one of the first construction processes to take place on a site.

## Slide 55
www.futuremanagers.com
INTRODUCTION
Setting out is perhaps the most important aspect of the early stages of the
construction process. It establishes the controlling dimensions and references from the architect's plans that will determine the positioning of the building, and in particular, the foundations. It ensures that the construction remains within the legal boundary, meaning there will be no legal dispute later on, such as those regarding property boundaries and right to access. This module details the instruments and methods involved in setting out.
Module 6: Setting out

## Slide 56
www.futuremanagers.com
DEFINITION OF SETTING OUT
Surveying is a process of forming maps and plans of a particular site or area.
Setting out is the transferring of details from the drawing to the ground.
Module 6: Setting out (continued)

## Slide 57
www.futuremanagers.com
Module 6: Setting out (continued)
CONSTRAINTS IN SETTING OUT A BUILDING
• A sloping site – sloping sites have to be levelled before any setting out can commence.
• A scrub site – a site with vegetation, bushes, trees, etc. will have to be cleared
before setting out, as they may present challenges during measuring.
• Site boundary pegs not visible – boundary pegs are used to identify the land
boundaries and to establish the exact position of the building.
• Weather conditions – rainy or windy conditions can make it difficult to measure or to read instruments.

## Slide 58
www.futuremanagers.com
Module 6: Setting out (continued)
SETTING OUT AND LEVELLING DRAINAGE WORK
To control the excavation of drainage or sewer trenches, sight rails are set up
above the existing ground level, such that the line of sight between the top of any pair of sight rails is parallel to the gradient of the trench bottom. Sight rails are fixed exactly horizontal at a precise level, using a levelling instrument. In order to achieve this, the staff reading is calculated by finding the difference between the collimation height and the sum of the invert level and height of travel.

## Slide 59
www.futuremanagers.com
Module 6: Setting out (continued)
SLOPE RATIO OF DRAINAGE OR SEWER PIPES
Slope ratio refers to the amount of slanting horizontally for every 1 m measured vertically.

## Slide 60
www.futuremanagers.com
Module 6: Setting out (continued)
SLOPE RATIO FORMULAE
Formula for calculating slope as a ratio:
Formula for calculating slope as a percentage:
Formula for calculating the length of the pipe:
Δh = difference in height between invert levels
Δchainage = difference in chainage (difference in distance between points).