## Slide 1
Building & Structural Surveying
N4

## Slide 2
www.futuremanagers.com
DEFINTION OF SURVEYING
Surveying may be defined as the art of taking measurements and making field observations that are necessary to determine the position, volumes and areas of all natural and/or man-made features on the earth’s surface and representing the results on a map or plan to a suitable scale.
Module 1: General

## Slide 3
www.futuremanagers.com
Module 1: General (continued)
PURPOSE OF SURVEYING
The purpose is to prepare survey drawings, such as maps, plans, cross sections or elevation drawings, with profiles which have all the necessary information about natural and manmade features. These are then used by the architect and the engineer to work on the design of the proposed structure. The final plan is then given to the surveyor who ‘sets out’ the work which might be construction projects such as roads, railways, reservoirs and buildings.

## Slide 4
www.futuremanagers.com
Module 1: General (continued)
TYPES OF SURVEYING
Different types of surveying include:
Plane surveying;
Topographic survey;
Cadastral surveying;
Engineering surveying; and
Geodetic surveying.

## Slide 5
www.futuremanagers.com
Module 1: General (continued)
METHODS (TECHNIQUES) OF SURVEYING
The following are the important methods:
Chain or taping survey;
Levelling;
Traverse survey (transit survey);
Tacheometric survey (Stadia surveying);
Triangulation survey;
Trilateration;
Compass survey;
Plane table survey; and
Photographic survey.

## Slide 6
www.futuremanagers.com
Module 1: General (continued)
QUALITIES OF A GOOD SURVEYOR
Must be neat, especially in booking field work.
Must possess initiative and approach each problem with resourcefulness.
Must accept information or results as trustworthy only after verification by an independent check.
Must be reliable and have sound judgement.
Must think clearly without confusion and reason logically without prejudice.
Must be thorough and content with his work.

## Slide 7
www.futuremanagers.com
Module 1: General (continued)
DIFFERENCE BETWEEN A BUILDING AND A LAND SURVEYOR
A building surveyor is involved in the survey buildings and structures, for the purpose of drawing plans for renovations or extensions of buildings and to ensure compliance with building regulations.
A land surveyor is involved in surveys for the purpose of developing maps, surveying land and buildings for the purpose of defining property boundaries and national boundaries, setting out and monitoring of roads, bridges, tunnels, large structures and railways.

## Slide 8
www.futuremanagers.com
Module 1: General (continued)
FUNCTIONS OF A SURVEYOR
The functions of a surveyor are divided into three areas, namely:
Field work;
Office work; and
Care and adjustment of instruments.

## Slide 9
www.futuremanagers.com
Module 1: General (continued)
PURPOSE OF FIELD WORK
It involves measuring distances and angles by handling and using survey instruments correctly.
Record field notes accurately using standard methods.
Details of the survey are located from reference points.
Directions are established.
Required structures and features and gradients are set out.
Relative elevation of points and inaccessible points are determined.

## Slide 10
www.futuremanagers.com
Module 1: General (continued)
FIELD BOOK
This is a small book used by a surveyor in the field to record survey data and notes as surveys are carried out. It should contain information such as:
Title page;
Index/index diagram;
Surveyor’s signature/Name;
Field party names;
Job description;
Observations;
Sketches;
Descriptions;
Equipment list; and
Weather information.

## Slide 11
www.futuremanagers.com
Module 1: General (continued)
SURVEY FIELD NOTES
Field notes are written notes of the field observations and measurements taken and recorded at the time the field work was done in the field. Due to the fact that other people will be reading the notes, a specific format is used for each type of survey carefully ensuring that the notes are clear and the format used can be easily interpreted by others.

## Slide 12
www.futuremanagers.com
Module 1: General (continued)
METHODS OF MEASUREMENT
Horizontal distance: measuring horizontally from one point to another.
Vertical distance: measuring to determine the height of a point.
Horizontal angle: measuring angles by moving the theodolite horizontally, to the left or to the right.
Vertical angle: measuring angle by moving the theodolite up or down.

## Slide 13
www.futuremanagers.com
Module 1: General (continued)
FUNDAMENTAL PRINCIPLES OF SURVEYING
The fundamental principle, upon which the various methods of surveying are based, is the determination of the relative positions of points; that is locating the horizontal position of a point with respect to at least two other points that are known.

## Slide 14
www.futuremanagers.com
MAPS
A map is the representation of a large section of the earth’s surface on a small scale with very little detail, onto a horizontal plane surface (sheet of paper). Although a map has a scale, not everything is drawn to scale, some parts on the map are represented by a dot which could represent a town in reality.
Module 2: Basic Concepts

## Slide 15
www.futuremanagers.com
Module 2: Basic Concepts (continued)
PLANS
A plan is the representation of the surface features of a small section of the earth’s surface drawn to a large scale onto a horizontal plane surface, showing more detail. All the parts on the plan are drawn to the scale indicated. The purpose of plans is to provide the detailed layout of a structure to be built or town layout indicating where residential houses, roads and shops will be.

## Slide 16
www.futuremanagers.com
Module 2: Basic Concepts (continued)
ACCURACY OF MAPS
The final form of a map or plan depends upon the purpose for which it is prepared. The scale depends upon the use to which the map or plan will be put. The smaller the scale, the less accurate the map will possibly be, to show the relative distances between two points.

## Slide 17
www.futuremanagers.com
Module 2: Basic Concepts (continued)
FACTORS INFLUENCING THE ACCURACY OF THE SURVEY
Control Framework;
Scale;
Speed and cost;
Skill and experience; and
Checks.

## Slide 18
www.futuremanagers.com
Module 2: Basic Concepts (continued)
MAP SCALES
The scale to which a map is drawn depends mainly on the use to which the map will be put. The greater the required degree of accuracy, the larger the scale, and certainly the more costly the map will be to produce. Types of scales:
Natural scale;
Engineering scale; and
Divided scale line.

## Slide 19
www.futuremanagers.com
Module 2: Basic Concepts (continued)
THE SOUTH AFRICAN CO-ORDINATE SYSTEM
The South African co-ordinate system is based upon the Gauss Conform Projection, also known as the Transverse Mercator Projection. This is an adaptation of the ordinary Mercator projection turned about 90° so that it may be based on any meridian not on the Equator. In South Africa the framework consists of a number of accurately co-ordinated trigonometric beacons covering the whole republic.

## Slide 20
www.futuremanagers.com
Module 2: Basic Concepts (continued)
ANGULAR MEASUREMENT
There are 3 types of angular measurement:
Sexagesimal;
Centesimal; and
Radian.

## Slide 21
www.futuremanagers.com
AREAS
When area needs to be calculated, it must be done in square metres. The Si unit for this is m².
Square and rectangle: Area = .
Trapezium: Area = .
Parallelogram: Area = .
Triangle: Area = .
Circles: Area = .
Module 3: Areas and Volume

## Slide 22
www.futuremanagers.com
Module 3: Areas and Volume (continued)
VOLUME
When calculating volumes, it will be noticed that the area calculation is done first, the area is then used with the depth to find the volume. The standard unit of measurement for volume is cubic metres (). The formula for calculating the volume is given as:
Volume = .

## Slide 23
www.futuremanagers.com
DEFINITION
Chain surveying uses a tape or chain as the principal instrument for the accurate of measurement of lengths. It involves the location of points by the measurement of the distance. The chain survey team involves the surveyor and two chain people, one being the leader and the other being the follower. The equipment used includes items for measuring lines, for marking stations or points, and for setting out simple angles.
Module 4: Chain Surveying

## Slide 24
www.futuremanagers.com
Module 4: Chain Surveying (continued)
LINEAR MEASUREMENT EQUIPMENT
The Chain;
Steel tape;
Synthetic tape; and
Surveyor’s folding ruler.

## Slide 25
www.futuremanagers.com
Module 4: Chain Surveying (continued)
MARKING EQUIPMENT
Chain arrows;
Ranging rods; and
Plumb rod.

## Slide 26
www.futuremanagers.com
Module 4: Chain Surveying (continued)
EQUIPMENT FOR SETTING OUT SIMPLE ANGLES
Cross staff:
Optical square:
Abney level:

## Slide 27
www.futuremanagers.com
Module 4: Chain Surveying (continued)
STEP CHAIN SURVEYING
Chaining may be done either on a horizontal plane or a sloping plane. When taping is done on a sloping plane, to obtain the horizontal distance of the slope, step chaining is used.

## Slide 28
www.futuremanagers.com
Module 4: Chain Surveying (continued)
IMPORTANT FACTORS IN DETERMINING THE SELECTION OF TRIANGLES
Triangle should be well conditioned (situated).
The number of lines should be kept to a minimum.
Lengths of offsets should be as short as possible.
Lines should free from obstruction.
All triangles must be provided with a check.

## Slide 29
www.futuremanagers.com
Module 4: Chain Surveying (continued)
OBSTACLES TO CHAINING (TAPING)
Chain lines should be arranged, as far as possible, to avoid obstructions, but there are obstacles that cannot be avoided, even after a careful preliminary survey. There are obstacles, such as a hill, which are obstacles to the line of sight but not to measurement, a pond, building, river or busy main road which are obstacles to measurement but not to sight. There are various methods that are applied to overcome these problems.

## Slide 30
www.futuremanagers.com
Module 4: Chain Surveying (continued)
ELECTRONIC DISTANCE MEASUREMENT (EDM)
The EDM is an instrument that measures distance using light and radio waves. The distance is measured by calculating the time difference between a transmitted pulse and a return pulse or the phase difference between a transmitted and a reflected beam of radiation.

## Slide 31
www.futuremanagers.com
ACCURACY AND PRECISION
“Accuracy” refers to how closely a measurement or observation is, to measuring a “true value,” since measurements and observations are always subject to error. “Precision” refers to how closely repeated measurements or observations come to duplicating measured or observed values.
Module 5: Linear Measurement Corrections

## Slide 32
www.futuremanagers.com
Module 5: Linear Measurement Corrections (continued)
ERRORS AND MISTAKES IN SURVEY MEASUREMENTS
Mistakes: Are avoidable blunders which occur because of carelessness or a temporary mental lapse. They include incorrect readings and booking of observations and the use of erroneous data in calculations.
Constant errors: Are those which have the same magnitude and algebraic sign. The errors can be caused either by the apparatus itself or external circumstances to the apparatus.

## Slide 33
www.futuremanagers.com
Module 5: Linear Measurement Corrections (continued)
ERRORS AND MISTAKES IN SURVEY MEASUREMENTS (CONT)
Systematic errors: Are errors which depend, for their magnitude and sign, upon external circumstances such as temperature changes, the slope of land etc., and they tend to produce cumulative effects.
Accidental errors: Are small errors in observation which cannot be detected by the human eye under normal surveying conditions. Accidental errors are human errors not caused by carelessness.

## Slide 34
www.futuremanagers.com
Module 5: Linear Measurement Corrections (continued)
TAPING ERROR CORRECTION
Measuring tape manufacturers do not usually guarantee the exact length of tapes; as a result tapes are standardised. Standardisation is a process whereby the standard temperature and tension are determined when the tape is the exact length.

## Slide 35
www.futuremanagers.com
DEFINITION
Levelling is determining the relative elevations or heights of points using a dumpy level or automatic level.
Module 6: Levelling

## Slide 36
www.futuremanagers.com
Module 6: Levelling (continued)
USE OF LEVELLING
It is used when highways, railroads, canals, sewers etc, are constructed.
Setting out of the elevation construction projects as indicated on the plan.
Heights determined are used to calculate the volume of earthworks and other materials.
Levelling is also used to investigate drainage characteristics of some areas.

## Slide 37
www.futuremanagers.com
Module 6: Levelling (continued)
LEVELLING EQUIPMENT
Traveller or boning rod;
Change plate;
Staff bubble;
Tripod stand;
Dumpy level;
Tilting level;
Automatic level; and
Bubble tube.

## Slide 38
www.futuremanagers.com
Module 6: Levelling (continued)
TELESCOPE FOCUSING
For accurate work when observing a target, both the cross-hairs of the reticule and the distant target object must be in sharp focus. This is done by focusing on the cross hairs first then the target, by bringing the image of the target object into exactly the same plane as the cross-hairs.

## Slide 39
www.futuremanagers.com
Module 6: Levelling (continued)
METHODS OF LEVELLING
There are three methods of levelling:
Differential levelling;
Trigonometric levelling; and
Barometric levelling.

## Slide 40
www.futuremanagers.com
Module 6: Levelling (continued)
LEVELLING PROCEDURE (FIRST POSITION OF THE LEVEL)
The level is set up at P where BM may be observed and readings taken at point A, B and C.
The first reading is taken with the staff on a point of known reduced level.
which is the benchmark. The reading is recorded as the back-sight.
The staff is held at A and B, in turn, and recorded as intermediate sights.
A change point is chosen at C owing to the nature of the ground. The reading is taken and recorded as the foresight.

## Slide 41
www.futuremanagers.com
Module 6: Levelling (continued)
LEVELLING PROCEDURE (SECOND POSITION OF THE LEVEL)
The staff remains at point C and the level is moved to Q, set up and levelled.
The reading on the staff at C, the change point, is taken and recorded as the BS.
Followed by intermediate sights D, E and F etc. until another change point is required.

## Slide 42
www.futuremanagers.com
Module 6: Levelling (continued)
THEODOLITE
This instrument is ideal for tacheometric and traverse surveying, but not for differential survey.

## Slide 43
www.futuremanagers.com
Module 6: Levelling (continued)
COLLIMATION ERROR
It occurs when the collimation line is not truly horizontal when the instrument is level. It is possible to determine the collimation error and reduce its size using the two peg test.

## Slide 44
www.futuremanagers.com
Module 6: Levelling (continued)
HANDS SIGNALS
The distance between the person operating the levelling instrument and the person holding the staff is sometimes huge. With one person being far away from the other, the best way of communication is to use hand signals.

## Slide 45
www.futuremanagers.com
DEFINITION OF COMPASS SURVEYING
Compass surveying is the location of points by measuring compass bearings (angles). It is used to ascertain magnetic north, direction.
Module 7: Compass Surveying

## Slide 46
www.futuremanagers.com
Module 7: Compass Surveying (continued)
PRINCIPLE OF COMPASS SURVEYING
The principle of surveying is traversing, which consists of a number of connected survey lines. The lengths of the legs are measured with a chain and the directions are measured with an angle measuring instrument. In one of the traverse methods, the angles are measured with a compass, hence the method is called compass traversing.

## Slide 47
www.futuremanagers.com
Module 7: Compass Surveying (continued)
MAGNETIC COMPASSES
There are two main types of magnetic compasses used in surveying; the surveyor’s compass and the prismatic compass. The surveyor’s compass is usually the larger and more accurate instrument, and is mostly used on a stand or tripod. The prismatic compass is often a small instrument which is hand-held for observing and thus employed in less accurate work.

## Slide 48
www.futuremanagers.com
Module 7: Compass Surveying (continued)
SYSTEMS USED TO EXPRESS BEARINGS
Whole circle bearing (WCB): This is the bearing of a line measured in a clockwise direction from true north towards the line and varies from 0 to 360 degrees.
Quadrantal Bearing (QB): In this system the bearing of a line is measured eastward or westward from north or south whichever is nearer. The directions can be either clockwise or anti clockwise depending upon the position of the line.

## Slide 49
www.futuremanagers.com
Module 7: Compass Surveying (continued)
DETERMINATION OF MAGNETIC BEARING AND TRUE BEARING
Magnetic bearing of a line is the bearing of a line measured from the magnetic north. It can be given as a WCB measured from true north or QB, but when calculating the true bearing the QB must be converted to WCB.
True bearing of a line is the horizontal angle between true north and the survey line. It is measured from true north in a clockwise direction. It can be given as a WCB or QB.

## Slide 50
www.futuremanagers.com
DEFINITION
Plane table surveying involves the measurement of distance and angles while plotting these observations simultaneously in the field. Although plane table surveying is not as accurate as other methods, but for certain types of work it gives sufficient accuracy. Methods used in plane tabling involve traversing, radiation, intersection and resection.
Module 8: Plane Table Surveying

## Slide 51
www.futuremanagers.com
Module 8: Plane Table Surveying (continued)
IMPORTANT POINTS WHEN SETTING UP THE PLANE TABLE
The table should be level when erected and oriented accurately.
The table should be at a workable height.
Keep all the equipment to be used on hand.
Select well defined stations for orientation.
Select stations that are recognised on the map.
Each ray should be easily identified.
Use reference numbers to refer to each ray.

## Slide 52
www.futuremanagers.com
Module 8: Plane Table Surveying (continued)
THE USE OF PLANE TABLE SURVEYING
There are uses why tolerable accuracy can obtained:
Production of maps and plans of small areas.
For the preparation of reconnaissance and exploratory survey maps.
Filling details between control points established more accurate by theodolite traverse or triangulation.
When existing maps and plans are reviewed.
For the location of contours.

## Slide 53
www.futuremanagers.com
Module 8: Plane Table Surveying (continued)
PLANE TABLE EQUIPMENT
Plane table;
Alidade;
Plane table compass;
Plumbing fork; and
Plane table spirit level.

## Slide 54
www.futuremanagers.com
Module 8: Plane Table Surveying (continued)
SETTING UP THE PLANE TABLE
Setting up the plane table consists of the following:
Centring (positioning) the plane table.
Levelling the plane table.
Orienting the plane table.

## Slide 55
www.futuremanagers.com
Module 8: Plane Table Surveying (continued)
METHODS INVOLVED IN PLANE TABLING
There are four main methods of surveying with a plane table:
Radiation.
Triangulation (intersection).
Traversing.
Resection.